FIRE EMISSIONS

(June 2011)

Fire emissions data for SMOKE have traditionally been represented as county-level area-source inventories that were placed in only the first vertical model layer. The representation of fire emissions for air quality modeling was enhanced by preparing the inventory data as point sources with specific latitude-longitude coordinates for each fire centroid and pre-computed plume rise parameters that were derived from individual fire characteristics. These new inventories consist of annual, daily, and hourly IDA-formatted emissions inventory files and ancillary data for allocating the inventories in space, time, and to the Carbon Bond-IV chemistry mechanism used in CMAQ and CAMx. The development of the fire emissions inventory is described in this section.

Source Categories

The fire emission inventories developed for the WRAP modeling efforts were organized into the following individual categories:

| Wildfires Agricultural fires Wildland fire use Natural prescribed | Anthropogenic prescribed Non-federal rangeland fires Non-WRAP fires |
| --- | --- |

For the non-WRAP fire emissions inventory, most of the data were modeled as area sources, with the exception of fire emissions for Canada, which were treated as elevated point sources.

The development of the fire emission inventories is described below. The discussion focuses on the development of the 2002 Base inventory (Base02); emissions modeling for the 2002 Planning inventory (Plan02) and the 2018 base year inventory (Base18) use the same processing approach. Variations to the modeling approach and specific revisions and enhancements incorporated into the final modeling versions of the inventories have been described previously (refer to the Emission Overview Documentation). Specific revisions are noted with respect to data sources and source categories for the Plan02 and Base18 emissions inventories.

Data Sources

Base02

Several regional fire inventories were used to build the Base02 inventory: actual 2002 data as developed by the RPOs for the U.S.; version 2 of the year 2000 Canadian inventory; and actual 2002 data for Ontario, Canada. There were no fire emissions in the BRAVO 1999 Mexico inventories, so Mexican fires were not included in the Base02 inventories. The inventories used consisted of both area- and point-source data for the U.S. and Canada. Air Sciences Inc. provided the WRAP inventories divided among six different fire categories: wildfires, agricultural fires, wildland fire use, natural prescribed, anthropogenic prescribed, and non-Federal rangeland fires (Air Sciences Inc., 2005). These inventories consisted of annual, daily, and hourly IDA-formatted files with information on daily emissions totals and hourly plume characteristics for each fire. Similar point source fire inventories for the VISTAS states were received from Alpine Geophysics (Stella, 2005). In addition, county-level fire inventories represented as area sources for the VISTAS and CENRAP states were included. Monthly temporal profiles received from Alpine Geophysics were used to distribute these annual inventories throughout the year. The area source inventories for the rest of the RPOs and Canada also contained fire emissions that were not distributed separately. These sources were modeled with the rest of the stationary-area-source sector. Finally, a 2002 fire inventory for Ontario, Canada, was received from MANE-VU and formatted to take advantage of the SMOKE fire plume rise algorithm (Pouliot et al., 2005).

Plan02

For the development of the Plan02 inventory, the RMC received corrected U.S. data for portions of the Base02 regional inventories. The previous inventory data for the affected areas were removed from the files used in the Base02 modeling; the remaining data were combined with the updated information to build revised Base02 inventories. The resulting dataset was used to develop the Plan02 inventory. This substitution of only the revised portions of the inventories was a general approach applied to several emissions sectors.

The updated information, provided by Air Sciences Inc., consisted of annual Baseline Phase III fire inventories for the WRAP region for each of five fire categories (wildfire, agricultural, wildland fire use, prescribed, and non-Federal rangeland) as three-file sets for each category. Consistent with the fire inventories for Phases I and II, each fire category consisted of an annual IDA file with physical fire event information, a daily IDA file with daily emissions by criteria pollutant, and an hourly IDA file with hourly pre-computed plume rise values. Upon receiving these data, the annual inventories were split into monthly files to avoid computer memory problems related to processing very large inventories with SMOKE. Additional information on the development of these fire inventories is available in Development of 2000-2004 Baseline Period and 2018 Projection Year Emission Inventories (Air Sciences, 2007).

Base 18

Baseline fire emission inventories for 2018 (Base18a) for WRAP, CENRAP, and VISTAS were held constant at Plan02 emission levels. For the 2018b inventory, a number of revisions were incorporated as follows:

- The WRAP inventories for prescribed and agricultural fires were updated and errors corrected in the application of temporal and speciation profiles for non-Federal rangeland prescribed fires.

- Air Sciences Inc. provided revisions to the Phase III prescribed and agricultural fire inventories to estimate the emissions reductions from applying fire emissions reduction techniques (ERTs) to controllable fire emissions (Air Sciences Inc., 2006). They based the revised emissions on the same data that the RMC used in case Plan02b to illustrate the changes that resulted from controlling prescribed and agricultural fires between the Plan02b and Base18b emission scenarios.

- The temporal and speciation profiles applied to the non-Federal rangeland prescribed fires were corrected. By not adding the SCC for this source to the input cross-reference files in the Plan02 and Base18a inventories, default temporal and speciation profiles were mistakenly applied to these emissions. The appropriate cross-reference for this source was added to the SMOKE input files in case Base18b.

Emissions Processing

SMOKE is instrumented to distribute point-source-formatted fire inventories to the vertical model layers either by using a pre-computed plume rise approach or by computing the plume rise dynamically using actual 2002 meteorology. Both approaches for modeling point source fire emissions were applied for the Base02 inventories. For the pre-computed plume rise approach, SMOKE reads an annual inventory file with information on fire locations, a daily inventory file with daily emission totals for each fire, and an hourly inventory file with hourly plume bottom, plume top, and layer 1 fractions for each fire. SMOKE uses this information to locate the fires on the horizontal model grid and to distribute the plume of each fire vertically to the model layers. Because some of these fires have plumes that reach the model top, the number of emissions layers for processing these inventories are set to the full 19 layers of the meteorology. This approach was applied to the point-source fires for the WRAP and VISTAS regions.

The alternative plume rise approach uses information on fuel loading and the heat flux of the fires to distribute the fires vertically to the model layers. The data are provided to SMOKE in the form of an annual inventory with information on fire locations and a daily inventory with daily emission totals for each fire, daily heat flux, and daily fuel loading. This approach to the point source fires was applied for Ontario, Canada.

All of the point-source fires used diurnal temporal profiles and speciation profiles for VOC and PM2.5 developed by Air Sciences during the preliminary 2002 modeling (Tonnesen et al., 2005).

For the area source fires outside of the WRAP region, including Canada, monthly temporal profiles developed by VISTAS were applied. While these profiles appear to be an improvement over the EPA defaults, they are specific to the VISTAS region and will misrepresent the seasonality of the fires in other regions of the modeling domain. Flat weekly temporal profiles, and the diurnal profiles developed by Air Sciences were also used in the fire emissions modeling. In addition, the forestland spatial surrogates were used to distribute these county level (province level for Canada) data to the model grid. Using spatial surrogates to locate fires is a crude approach that results in the artificial smearing of the emissions over too large an area. Both of these issues can be remedied by moving to a point source approach for representing these fires, similar to the approach used by Air Sciences Inc. for preparing the WRAP fire inventories.

The RMC discovered several errors with the WRAP Phase II inventories. Some of these errors were fixed with corrections made by the RMC with guidance from Air Sciences Inc., and others were addressed by Air Sciences Inc. in Phase III of the 2002 WRAP fire inventories. The errors identified, with corrections, were as follows:

- Missing or malformed dates in several agricultural burning events in CA. These events were intended to be dropped and were ultimately deleted from the inventories by the RMC.

- Missing dates in several prescribed burning events in AZ. These records were corrected by Air Sciences Inc. and redistributed to the RMC.

- Inconsistencies between the records in the hourly and annual inventory files for several agricultural burning events in CA. These records were corrected by Air Sciences Inc. and redistributed to the RMC.

The quality assurance of the fire emissions followed the WRAP emissions modeling QA protocol (Adelman, 2004) and a suite of graphical summaries. Tabulated summaries of the input data and SMOKE script settings were used to document the data and configure SMOKE. The graphical QA summaries include, for all emissions output species, daily time-series plots, annual time-series plots, and daily vertical profiles. These QA graphics for the 2002 inventories are available at http://pah.cert.ucr.edu/aqm/308/QA_base02a36.plots/allf/plots/.

Gridded Fire Emission Inventory Summaries

Summaries of the gridded fire source emissions for the Base02b, Plan02c, Plan02d, Base18b, and PRP18a inventories by state and county, annual and seasonal periods, can be found on the TSS at:  http://vista.cira.colostate.edu/tss/Results/Emissions.aspx.

References

Adelman, Z. 2004: Quality Assurance Protocol – WRAP RMC Emissions Modeling with SMOKE, Prepared for the WRAP Modeling Forum by the WRAP Regional Modeling Center, Riverside, CA.

Air Sciences Inc., 2005: 2002 Fire Emission Inventory for the WRAP Region – Phase II, prepared for the Western Governors Association/WRAP by Air Sciences, Inc., Denver, CO. Available at: http://www.wrapair.org/forums/fejf/documents/WRAP_2002_PhII_EI_Report_ 20050722.pdf.

Air Sciences Inc., 2006: Technical Memorandum: Fire Emissions Inventory – Phase III Base-Control Case, Prepared for Western Regional Air Partnership Fire Emissions Joint Forum Air Sciences Inc., April 28, 2006.  Available at: http://www.airsci.com/wrap/phase3-4/ Fire_EI_Base_CC_20060428.pdf.

Air Sciences Inc. and ECR, Inc., 2007: Development of 2000-04 Baseline Period and 2018 Projection Year Emission Inventories, prepared for the Western Governors Association/WRAP by Air Sciences, Inc., Denver, CO. Available at: http://www.wrapair.org/ forums/fejf/documents/task7/Phase3-4EI/WRAP_Fire_Ph3-4_EI_Report_20070515.pdf.

Pouliot, G., T. Pierce, W. Benjey, S.M. O’Neill, and S.A. Ferguson, 2005: Wildfire Emissions Modeling: Integrating Blue Sky and SMOKE, in Proceedings of the 14th Annual Emissions Inventory Conference, Atlanta, GA.

Stella, G., 2005: Base F Emissions Inventories by State and RPO, Prepared for the VISTAS Joint Work Group Meeting by Alpine Geophysics, LLC. http://www.vistas-sesarm.org/documents/ VISTASJointWorkGroupMeeting09052005/2_Stella-IPM2018Results22Sept2005.ppt.

Tonnesen, G. et al., 2005: Final Report for the WRAP RMC for the Project Period March 1, 2004 through February 28, 2005, Prepared for the Western Governors Association by ENVIRON International Corporation, Novato, CA. Available at: http://pah.cert.ucr.edu/aqm/308/ppt_files/emissions/nh3/Volume_I_FinalReport.3-07.pdf.