IMPROVE PARTICULATE MONTORING

Background

The Interagency Monitoring of Protected Visual Environments (IMPROVE) monitoring program collects speciated PM2.5, and PM2.5 and PM10 mass.  IMPROVE is a nation-wide network which began in 1988 and expanded significantly in 2000 in response to the EPA’s Regional Haze Rule (RHR).  The Regional Haze Rule specifically requires data from this program to be used by states and tribes to track progress in reducing haze.  The primary purposes of the IMPROVE network are to:

- Establish current visibility and aerosol conditions in mandatory Class I areas;

- Identify chemical species and emission sources responsible for existing man-made visibility impairment;

- Document long-term trends for assessing progress towards the national visibility goal;

- Provide regional haze monitoring representing all visibility-protected federal Class I areas where practical, in support of the Regional Haze Rule.

A listing of site affiliations, names, abbreviations, locations, and operational start dates is presented in Table 1.  Some Class I areas do not operate aerosol samplers but are represented by samplers located at other, nearby Class I areas.  The representative monitoring site for each Class I area is indicated in the Site Name and Site Code fields in Table 1.

Detailed information regarding the IMPROVE program, including history, sampling protocols, standard operating procedures, and data availability can be found on the IMPROVE Web site (http://vista.cira.colostate.edu/improve/) and the Visibility Information Exchange Web System (VIEWS) Web site (http://vista.cira.colostate.edu/views/).

IMPROVE Sampling and Analysis Protocols

The design of the IMPROVE network and sampling procedures is dictated by the network goals, the need to control costs, maintain consistency, and the often remote locations of the monitoring sites.  The IMPROVE network collects 24-hour integrated filter samples every three days (Wednesday and Saturday prior to 2000).  Each monitoring location operates 4 samplers.  Modules A through C employ PM2.5 size-cut devices, and Module D a PM10 size-cut device.  The analysis techniques and major visibility-related species associated with each module type are described below.

Module A utilizes a Teflon filter for PM2.5 gravimetric and elemental analysis.  Gravimetric analysis relies on the difference in weight between a clean (new) and loaded (used) filter to determine the total amount of particulate collected (total PM2.5).  The elemental analysis is done in two ways.  Proton Elastic Scattering Analysis (PESA) is used to determine the concentration of hydrogen (H) on the filter.  X-ray Fluorescence (XRF) is used to determine the concentration of elements from sodium (Na) to zirconium (Zr) and lead (Pb).  Prior to December 2001 Particle-Induced X-ray Emission analysis was used to analyze for the lighter elements (through manganese, Mn).  This technique was replaced by XRF to attain better detection limits.

Table 1

Site Specifications

### IMPROVE Network – WRAP Region

(cont.)

Table 1 (cont.)

Site Specifications

### IMPROVE Network – WRAP Region

The visibility-related species derived from this Module A are:

- Ammonium sulfate (derived from measured sulfur)

- Soil (derived as a weighted sum of selected elements)

- Coarse mass (in conjunction with module D)

- Sea salt (backup measurement derived from chlorine)

Module B utilizes a nylon filter preceded by a carbonate denuder for PM2.5 ion analysis.  The denuder removes gaseous nitric acid (HNO3) from the sample stream to avoid capturing is on the filter and incorrectly including it in the nitrate measurement.  Sample filters are subjected to ion chromotragraphy to identify concentrations of various negative ions.  The visibility-related species derived from Module B are:

- Ammonium nitrate

- Sulfate (backup measurement)

- Sea salt (derived from chloride)

Module C utilizes a quartz filter for PM2.5 carbon analysis.  Organic and elemental carbon are measured using the Thermal Optical Reflectance (TOR) method, in which the sample is subjected to a series of temperature steps, first in a 100% helium atmosphere (to evolve particulate carbon to gaseous form), then in a 98% helium, 2% oxygen atmosphere (to burn off the remaining original carbon and the carbon pyrolized during the first stage.  Carbon detected during the 100% helium atmosphere, and a portion detected once oxygen is introduced is interpreted as organic carbon, defined by the reflectance of the sample.  The remaining carbon is interpreted as elemental carbon.  The important visibility-related species derived from Module C are:

- Organic mass (derived from measured organic carbon)

- Elemental carbon

Module D utilizes a Teflon filter for PM10 gravimetric analysis.  The difference between module D PM10 and module A PM2.5 yields an estimate of coarse mass.  (Module D filters can be analyzed for elements in a manner identical to module A filters, but this is not done on a routine basis.)  The important visibility-related species derived from Module D is:

- Coarse mass (in conjunction with module A)

Table 2 presents a brief history of major historical changes in IMPROVE program protocol since its inception.  Of particular importance are those changes which have occurred during the RHR baseline period, 2000-04.

Table 2

Major Historical Changes in IMPROVE Protocol

IMPROVE Uncertainty Estimates

There are some uncertainties easily measured for each sample, including those associated with sample flow, sample duration, and laboratory analysis.  These uncertainties can be found in each record of the IMPROVE data set.  There are also uncertainties that are not easily measured, such as the estimation of extinction for a specific day, or how well a 24-hr sample taken once every three days represents an episode lasting several hours or many days.  The second category of uncertainties can generally only be understood by reviewing other data beyond that collected by IMPROVE.

The sample flow is critical to proper size cut.  A low flow will increase the size fraction captured; a high flow will decrease it.  IMPROVE PM2.5 mass measurements are considered valid within a large range of the flow rate required for a 2.5 µm cut.  A 7% deviation in flow rate will result in a shift in cut point down to 2 or up to 3 µm.  Concentration data associated with average flow rates greater or less than 7% of expected, or contain hourly peak or minimum flows that are as much as 17-20% off are flagged as exceptionally high/low flow rates, but the data are considered valid.  There can be substantial errors in calculating coarse mass if the PM2.5 sampler flow rate was significantly out of the expected range.

Laboratory uncertainties and minimum detectible limits for each sample are included in the IMPROVE data set.  A review of all WRAP region IMPROVE data (except for sea salt) for the baseline period yielded the median laboratory uncertainties listed in Table 3.  These uncertainties do not take into account sample flow or duration errors.

Table 3

Median Uncertainty of IMPROVE Data across WRAP

2000-04

Estimation of Light Extinction

Light extinction, or the fraction of light lost per unit length along a sight path due to scattering and absorption by gases and particles, can be estimated from speciated aerosol and relative humidity data.  Each major species is assigned a dry mass extinction efficiency.  This accounts for the fact that an elemental carbon particle is ten times more efficient at absorbing light than a particle of soil is at scattering light.  The sum of species mass for a given sample will not necessarily agree with the gravimetric mass (determined by weighing the filter) due to assumptions based on average values, which may be inaccurate on a given day or under certain circumstances.  IMPROVE makes the assumption that all sulfur and sulfate ions measured existed in the atmosphere as ammonium sulfate.  In reality, there are other forms of particulate sulfate, and the mix of sulfate types affects both the total sulfate mass and its contribution to extinction.  IMPROVE makes the assumption that all nitrate ions measured existed in the atmosphere as ammonium nitrate.  Some nitrate may be in other forms, though the percentage on a given sample or the annual average at individual sites is not currently known.

Sulfate and nitrate species are known to absorb water and thus their contribution to extinction is enhanced above certain values of relative humidity (RH) as the particles increase in size.  As the RH increases, IMPROVE assumes an increase in scattering by these species.  EPA RHR guidance and current IMPROVE protocol call for the use of a “climatologically representative” monthly average f(RH) enhancement factor.  This approach removes much of the short-term variability of RH effects and allows calculation of extinction at sites which do not routinely monitor RH.  However, extinction calculated using a long-term average of RH will likely not represent the actual visibility conditions on a given day.

Table 4 presents a list of the major visibility-related species from the IMPROVE data set and how they are calculated.  The measured and derived mass quantities are listed first (lines 1-14), followed by the derived quantities required to estimate extinction (lines 15 – 28).  Extinction can be calculated using either the “old” or “new” IMPROVE algorithm and the table refers to both of these algorithms as required.

IMPROVE data were first used in 1993 to estimate extinction, using what is now referred to as the old IMPROVE algorithm, the equation shown in line16 of Table 4.  The algorithm performs reasonably well over a broad range of particle extinction, but tends to underestimate the highest extinction values and overestimate the lowest extinction values, as measured by ambient nephelometers and transmissometers.  This algorithm was in effect at the time of the writing of the Regional Haze Rule, and adopted by the EPA as the basis for the RHR visibility metric.

As regional planning organizations (RPOs) and industry stakeholders began to investigate the IMPROVE data set closely with regard to the Regional Haze Rule requirements, it was suggested that certain aspects of the old algorithm should be modified to better represent the state of visibility science.  A review team, consisting of scientists from the National Park Service (NPS) and the Cooperative Institute for Research in the Atmosphere (CIRA), developed a revised algorithm, generally referred to as the new IMPROVE algorithm.  The review team relied on an extensive literature review and comparison of aerosol-estimated scattering with measured scattering from 21 nephelometers collocated with aerosol samplers across the network.  The new algorithm was adopted by the IMPROVE steering committee in December 2005.  EPA has not modified its guidance documents to indicate adoption of the new algorithm, but the WRAP and other RPOs have chosen to use it as the basis for their 2007 Regional Haze SIPs.

The new IMPROVE algorithm is shown in line 15 of Table 4.  The changes from the old to new algorithm include:

- The extinction efficiencies for ammonium sulfate, ammonium nitrate, and organic mass constituents are variable in nature, so each component mass has been split into a large and small fraction (see lines 17 – 22).  To each fraction is applied a unique dry extinction efficiency and scattering enhancement factor (see lines 23 – 26).  In the WRAP region, where sulfate and nitrate levels are generally low and predominantly modeled as the “small fraction,” this often results in lower extinction due to these two components.  Organic mass can be very high during fire season, with the result that many samples associated with file are modeled as the “large fraction.”

- The multiplier used to calculate organic mass from organic carbon was changed from 1.4 to 1.8 (see line 7).  The organic carbon literature indicates that the new multiplier is more realistic, particularly for rural areas.  This change increases the estimate of organic mass at all sites regardless of region.

- The addition of a sea salt term derived from chloride (see line 13).  Sea salt is hygroscopic so a scattering enhancement factor, fss(RH), is required (see line 26).  The assumption that all measured chloride originated as sea salt may not be correct for every site, and the network sampling change to a new supplier of nylon filters for Module B on January 1, 2004, can be seen as a step function in the chloride data record.  Scattering due to sea salt is significant only at coastal sites.

- Rayleigh scattering, or natural atmospheric scattering, has changed from a network-wide constant of 10 Mm-1 to a site specific value of 8 – 12, depending on elevation (higher elevations are associated with lower Rayleigh scattering) (see line 28).  This makes a small difference at WRAP sites, particularly on the clean days.

- Addition of a nitrogen dioxide (NO2) absorption term (see line 14), as this is the only common gaseous pollutant to significantly contribute to haze.  This is an optional term in the new algorithm, and since IMPROVE sites are not generally collocated with NO2 monitoring sites this term is not used in the processing of IMPROVE data for visibility.

The largest implications for the WRAP region of using the new IMPROVE algorithm to estimate light extinction are:

- The new algorithm is better at representing the cleanest and haziest days than the old algorithm, but with a loss of precision (higher data scatter) throughout the full range of extinction.

- Overall, the majority of WRAP region sample days (~85%) show a slightly lower extinction with the new algorithm (a distribution of algorithm differences is centered at -2 Mm-1).  This is largely due to the fact that relatively few organic mass samples contain significant large fraction mass (except during fire episodes), and very few ammonium sulfate and ammonium nitrate samples contain significant large fraction mass.

- Organic mass collected during large fire episodes contributes significantly more towards total extinction under the new algorithm than the under the old, due to the higher organic mass multiplier and the dominance of the large fraction during these episodes.

- With the introduction of sea salt scattering in the new algorithm, extinction at coastal sites has increased from estimates made with the old algorithm.  Sea salt is now a significant contributor at a few WRAP IMPROVE sites.

More information about the new IMPROVE algorithm can be found in the IMPROVE Newsletter, 4th Quarter 2005:

http://vista.cira.colostate.edu/improve/publications/NewsLetters/IMPNews4thQtr2005.pdf.  The final report on the new IMPROVE algorithm by the review committee can be found at:  http://vista.cira.colostate.edu/improve/publications/graylit/016_IMPROVEeqReview/IMPROVEeqReview.htm

Table 4

Determination of IMPROVE Species Required for Extinction Calculation

(cont.)

Table 4 (cont.)

Determination of IMPROVE Species Required for Extinction Calculation

IMPROVE Data Completeness in the WRAP Region

In the WRAP states, data substitution was performed for nine IMPROVE monitoring sites to achieve RHR data completeness, or to fully populate 2002, WRAP’s selected modeling year.  These data substitutions included estimating missing species from other on-site measurements and appropriately scaling data collected at selected donor sites which had favorable long-term comparisons.  While a brief overview of this process is given here, a full description of these methods can be found at:  http…

RHR guidance (http://www.epa.gov/ttn/oarpg/t1/memoranda/rh_tpurhr_gd.pdf.) outlines IMPROVE aerosol data completeness requirements including the following conditions:

- Individual samples must contain all species required for the calculation of light extinction (sulfate, nitrate, organic carbon, elemental carbon, soil, coarse mass, and, for the new IMPROVE algorithm, chloride or chlorine).

- Individual seasons must contain at least 50% of all possible daily samples.

- Individual years must contain at least 75% of all possible daily samples.

- Individual years must not contain more than 10 consecutive missing daily samples.

- The baseline period (2000-04) must contain at least 3 complete years of data.

RHR guidance also provides provisions to fill in missing data under specific circumstances. There are currently two methods routinely used in preparing the RHR data set to substitute data for missing samples:

- The use of a surrogate in the data set:

- Total sulfate is generally determined as 3 times the sulfur measured on the A module filter.  If sulfur is missing, the sulfur measurement from the B module filter is used to calculate sulfate.

- For the new IMPROVE algorithm, sea salt is calculated from chloride measured on the B module filter.  If chloride is missing or below detection limit, the chlorine measurement from the A module filter is used to calculate sea salt.

- The application of “patching” missing data described by the RHR guidance:

- Missing samples not substituted using a surrogate as described above can be patched, or replaced, by a seasonal average if the patching exercise passes a series of tests outlined in the guidance document.

Once these methods have been applied to the data, the resulting complete years are eligible for use in calculation of baseline conditions and tracking progress under the Regional Haze Rule.

These methods were applied to all IMPROVE data, but some WRAP sites still failed to meet data completeness requirements for the baseline period.  These sites are listed in Table 5.  (Sites that did not meet data completeness requirements but were not necessary for submittal of State Implementation Plans (SIPs) are indicated with an asterisk (*) in Table 5.  Additional data substitution for these sites has not been applied.)  Sites were candidates for substitution for two reasons:

- The sites had fewer than 3 complete years of data, thus RHR visibility metrics for the baseline period could not be calculated.

- The sites had at least 3 years of complete data, but were missing 2002, the year selected for regional modeling.  If this year is missing, then the worst 20% visibility days from 2002 cannot be determined, and the relative response factors (RRFs), which are used to predict visibility metrics in 2018, cannot be calculated.

Note that only years deemed incomplete under RHR guidance were candidates for additional data substitutions.  Years deemed complete were not changed, even thought there may have been missing samples during those years.

Table 5

WRAP Sites Failing RHR Data Completeness Requirements

| State | Site | <3 years | Missing 2002 |
| --- | --- | --- | --- |
| AZ | BALD1 | X | X |
|  | INGA1* | X | X |
|  | TONT1 |  | X |
| CA | KAIS1 | X | X |
|  | RAFA1 | X | X |
|  | SEQU1 |  | X |
|  | TRIN1 |  | X |
| MT | FLAT1* | X | X |
|  | FOPE1* | X | X |
|  | GLAC1 |  | X |
|  | NOCH1* | X | X |
| UT | CAPI1 | X | X |
| WA | NOCA1 | X |  |

* Indicates additional substitution is not required for a SIP.

The first of the additional substitution methods used organic hydrogen as a surrogate for organic carbon, and resultant organic carbon as a surrogate for elemental carbon.  If the carbon data substitution was not sufficient to complete the required years, measured mass for individual species from nearby IMPROVE sites with favorable long-term comparisons were scaled appropriately and used as surrogates.  IMPROVE donor sites were selected in consultation with individual states.  All site-to-site substitutions were made using quarterly-specific Kendall-Theil linear regressions statistics.  These statistics were chosen because they are more resistant to outliers than the standard linear least squares statistics.

Table 6 indicates which years required some degree of substitution, where a 2 indicates a substituted year, a 1 indicates the year was already complete under RHR guidelines, and dashes indicate the year did not meet RHR guidelines and no additional substitutions were made.  The table also lists sites that were selected as donor sites.

Table 6

Data Completeness at WRAP Sites Following Data Substitution

| State | Site | <3 years | Missing 2002 | Donor | 2000 | 2001 | 2002 | 2003 | 2004 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| AZ | BALD1 | X | X | TONT1 | -- | 2 | 2 | 1 | 1 |
|  | TONT1 |  | X | SIAN1 | -- | 1 | 2 | 1 | 1 |
| CA | KAIS1 | X | X | YOSE1 | -- | -- | 2 | 1 | 1 |
|  | RAFA1 | X | X | PINN1 | 2 | 2 | 2 | 1 | 1 |
|  | SEQU1 |  | X | DOME1 | 1 | 1 | 2 | 2 | 1 |
|  | TRIN1 |  | X | LAVO1 | -- | 1 | 2 | 1 | 1 |
| MT | GLAC1 |  | X | FLAT1 | 1 | 1 | 2 | 2 | 1 |
| UT | CAPI1 | X | X | CANY1 | 2 | 2 | 2 | 1 | 1 |
| WA | NOCA1 | X |  | SNPA1 | -- | 1 | 1 | 2 | 2 |

-- indicates an incomplete year with no substitutions made

1 indicates a complete RHR year

2 indicates a year is considered complete with some substituted values

The minimum data requirement of 3 complete years (including 2002) was met for each site, and additional substitutions beyond these requirements were made on a case by case basis in consultation with individual states.  For example, at the KAIS1 site, substitutions were made only for the 2002 year even though substituted data (from the YOSE1 donor site) was available for other years.  In this case, the years 2000 and 2001 had less than 50% of the original RHR data.  In contrast, additional substitutions were applied for all incomplete years (2000-2002) at the RAFA1 site.  For the RAFA1 site, the original RHR data was more substantial (73-86% available) and substitutions had less of an impact on the worst days distributions.

A dedicated page on the VIEWS web site is the repository of all site-specific substitute data sets:  http://vista.cira.colostate.edu/views/web/documents/substitutedata.aspx.  All materials prepared in the data substitution work (descriptive narrative, tables of regression statistics, graphics, etc.) are posted on this site for review by states, tribes, and other data users.  The substituted data sets are also accessible through the TSS.

Natural Condition Estimates

The Regional Haze Rule requires that visibility in all Class I areas reach natural conditions by 2064, implying no anthropogenic contributions to haze at that time.  As a practical matter, the haze levels associated with so-called natural condition are very difficult to define. RHR guidance (http://www.epa.gov/ttn/oarpg/t1/memoranda/rh_envcurhr_gd.pdf) outlines a default approach for determining natural conditions which include starting with natural annual species concentration estimates published in the 1990  National Acid Precipitation Assessment Program (NAPAP) State of Science and Technology, Report 24, by John Trijonis (http://matar.cira.colostate.edu/improve/Publications/Principle/NAPAP_SOS/High%20Res/napap_(high).htm), applying the old IMPROVE algorithm to estimate associated extinction levels, and applying various statistics to determine the appropriate natural conditions targets for the 20% haziest and 20% clearest days.  Numerous criticisms were made of the default approach, particularly once states began to adopt the new IMPROVE algorithm, under which the default approach cannot be used.  Since EPA guidance also allows for alternate natural conditions to be developed by states, provided that a reasonable argument can be made for their use, the Natural Haze Levels II Committee was established in 2006 to review and refine the default approach.  The committee included representatives from NOAA, NPS, CIRA, RPO and industry representatives, and other participants.  The final report of the committee can be found at:  http://wrapair.org/forums/aoh/meetings/060726den/NaturalHazeLevelsIIReport.ppt.

Unlike the default approach which directly uses the Trijonis natural species concentration estimates to calculate haze levels, the alternate approach adjusts the data set of current species concentration using a multiplier applied to each species measurement that gives the Trijonis estimate for that species.  The ratio of the Trijonis estimates for each species divided by the annual mean values for the species was used to transform the entire data set to what was then assumed to be the natural species concentration levels for that site and year.  This process was applied to each of the complete years of data in the baseline period.  Sites with 3 complete years of data were treated as having sufficient data for this assessment.  Provisional estimates were made for sites with fewer than three complete years.  If any of the current annual mean for any species was less than the Trijonis estimate for that species, the unadjusted species data were used.  Trijonis estimates do not include sea salt, which is only significant at a few coastal sites.  Estimates of current sea salt concentrations were taken to be natural contributors to haze.

The fundamental assumption inherent in this Natural Haze Levels II approach was that the Trijonis-adjusted species data set is a good estimate of the natural species data set.  Thus each site has its own a natural haze distribution which is derived from the current distribution, so no assumptions about the shape and width of the natural distribution are needed because there were sufficient values to actually calculate the 20% best and 20% worst means for site and year.  The new IMPROVE algorithm was applied to the Trijonis-adjusted concentration data, and the appropriate best and worst natural conditions estimates by individual species extinction and total deciview were generated.  Figure 1 presents a map of the U.S. contoured to show the worst 20% days natural conditions calculated from this alternate approach.

The natural conditions estimates determined by the Natural Haze Levels II approach are available on the VIEWS and TSS web site.  These values are integral to the TSS visibility glide slope and visibility projections tools.

Figure 1.  Estimates of the Worst 20% Natural Conditions using the Natural Haze Levels II Alternate Approach.

Visibility Metrics

The three most common metrics used to describe visibility impairment are extinction, visual range, and the haze index.  Figure 2 presents a comparison of these metrics on the same scale and a set of images with simulated visibility impairment.  As can be seen in the figure, an increase in extinction or haze index (deciview) is equivalent to a decrease in visual range.  The three metrics are defined as:

- Extinction – Extinction is a measure of the fraction of light lost per unit length along a sight path due to scattering and absorption by gases and particles, expressed in inverse Megameters (Mm-1).  This metric is useful for representing the contribution of each aerosol species to visibility impairment and can be practically thought of as the units of light lost in a million meter distance.

- Visual Range – Visual range is the greatest distance a large black object can be seen on the horizon, expressed in kilometers (km) or miles (mi).  Visual range can be calculated from total extinction by:

Visual Range (km) = 3912/Total Extinction (Mm-1)

- Haze Index (Deciview) – The Haze Index, measured in deciviews, was designed to be linear with respect to human perception of visibility.  A one deciview change is approximately equivalent to a 10% change in extinction, whether visibility is good or poor.  A one deciview change in visibility is generally considered to be the minimum change the average person can detect.  This is the metric used for tracking regional haze in the RHR.  The Haze Index can be calculated from total extinction by:

Haze Index (deciviews) = 10 x ln(Total Extinction/10)

Figure 2.  Comparison of the Deciview, Extinction (Bext), and Visual Range (V.R.) visibility metrics.  The six images of the West Elk Mountains were simulated to represent varying degrees of visibility impairment.